## Slide 1: RFVLSI Design Flow 2015 Upgrade Part-I RFSkill Programming Language: Design Cell Class/Placement
Yu-Jiu Wang
2015
(This is a quick internal documentation. Don’t follow this slides’ quality and format!)

## Slide 2: Current RFVLSI Design Flow
The blue part is already implemented in RFVLSI lab.
We cover green part in this slides.
Initial Theoretic Ideas
Ideal Symbolic Circuit
Symbolic Circuit with Parasitics
Pcell Libraries
EM Simulations
Physical Layouts
SPICE Equivalent Models
Some are ready.

## Slide 3: Current Flow Integrates Two EM Sim Approaches
Write a program based on HFSS Vbscript, and SonnetLab matlab scripting to automate EM simulation.
  Pro: design sweep, to find proper component dimensions.
  Cons: we need to “manually” check whether the HFSS/Sonnet codes are consistent with the layout.
Use cadence gds-export, HFSS/Sonnet gds-import functions to build EM simulations.
  Pro: always consistent with final layout.
  Cons: It is inflexible. Lots of human interference. We can only passively verify whether our current layout functions? But not to do a few dimension sweep to choose best layout design.

## Slide 4: Skill-to-EM translation?
RFVLSI lab has accumulated many layout pcell codes over the past two tapeouts.
During the two tapeouts, we find we bottlenecked at the layout-to-EM simulation step.
Idea, can we do this?
If possible, then we take advantages of our many layout codes, and seamly integrate them into many different EM simulation tools? (HFSS and Sonnet).
PCell SKILL codes
Skill-to-EM
Language
Translator
Sonnet Codes
HFSS Codes
HFSS Simulation
Sonnet
Simulation

## Slide 5: How a language translator works?
Note, SKILL, Vbscript and matlab has different language property. For example, the conditional operator is not supported in Vbscript: A?B:C, so the is no simple way to translate them.
However, if we limit our SKILL to an sufficient language subset, then we can do the translation with too much trivial overheads.
The translation process:
SKILL-codes
An Abstract Tree that represent the meaning of a SKILL code
HFSS or Sonnet Code

## Slide 6: Current Architecture
Input file6:
load(“pcell1.il”)
load(“pcell2.il”)
load(“pcell3.il”)
skill_to_hfss
GUI
SKILL code files:
Pcell1.il
Pcell2.il
Pcell3.il
Input file3:
Some process depedent
Codes from N65.il (Will faded out in the future.)
A Sim.vbs for a set of parameters ready for simulation
Input file1 & 2:
MetalStack.csv
DielectricStack.csv
Process/EM String Template
Generator
Process.stg
(Internal only, and invisible to GUI users)
Input file5:
HFSS.stg
(HFSS process independent template)
Input file4:
Process generic HFSS *.stg

## Slide 7: Drawbacks of current design flow
Synthesis/Schematic Design/Layout Design/EM/Model Fitting/Verification parts are not completely interconnected.
The underlying cadence Skill platform are not very safe:
  Dynamic Scoping
  Standard Turing machine computing model.
No object-oriented cell-level support which makes complex cell, such as power MOS layout very hard to debug.
No easy way for design reuse.
No unit-test(-like) support for large hierarchical design.
No useful analog design convex set formulation/optimization support.
No layout-to-readable codes to allow quick coding.
No modern IDE supports, etc.
No (N65/N40/N28/TN20..) process migration support.

## Slide 8: There types of basic problems in Design
Pattern Match,
for example:
  Verilog: And(net0, net1)  RTL netlist: AND gate  transistor-level netlist
2. Optimization problems
For example:
3. Routing Problems
For example:
opamp1.output.connectTo(opAmp2.input)
There are many choices that can achieve the above goal.
  Opamp.Idc< 10mA
  Opamp.Height=10um
  Opamp.gain> 60dB.
  Opamp.BW>1M
  Opamp.Width.minimized()

## Slide 9: Build an better underlying infrastructure, by redesigning the SKILL language
Safe and object-oriented physical design codes.
Layout/Schematic  high-level design codes .
Declarative testbench generation, that directly fitted into hierarchical design unit tests and measurement setups.
Cell-level design parameters-to-performance convex-set generation and optimization.
To create an better infrastructure, so a small team can deliver more productivity than bigger team through automation; and designers can focus their time on the essence of design, instead of implementation details.

## Slide 10: Dynamic  Lexical Scoping
Cadence SKILL(Dynamic Scoping)
X=1
dbCreateParamInst(nil evilvias 0:0 1
? SomeParameter 1)
dbCreateParamInst(nil vias 0:0 1
? SomeParameter X) // this X is 2.
------ the pcell definition
dbDefinePCell(
List(ggLib(“Lib”), “evilvias”, “layout”)
((SomeParameter 1))
X=2
)
New RFSkill (Lexical Scoping)
X=1
evilvias .place(0:0) with (
? SomeParameter 1)
vias.place(nil 0:0) with (
? SomeParameter X) // this X is always 1.
New compiler guarantee lexical scoping models.
New IDE checks for lexical scoping errors.

## Slide 11: Turing model  Evaluate & Substitute Model
Turing Model
Sum=0
For(i 1 5
Sum=sum+1 )
What is sum???
  We change the value of sum (which is stored in CPU register every iteration).
Very hard to debug; because the value of a variable depends on its context (the location of code).
Pretty bad when dynamic scoping is also used.
Evaluate & Substitute
All variables can only assigned once.
A=A+1 is not allowed.
A=2, B=3, C=4
D=(C+(B*A)) will be evaluated internally:
  D=(4+2*3)
  D=4+6
  D=10
Tree-type of execution model.
New IDE checks for the model problems.

## Slide 12: PCell as a Class
pcDefinePCell(
List(“Lib”, “Cell”, “View”)
(
(Param1 "1234")
(Param2 1234)
)
  Master=dbOpenCellView(“lib”,”vias”,”layout”)
  dbCreateParamInst(master 0:0 1
  ?width 1
  ?length 1
  )
  dbCreateParamInst(master 2:0 1
  ?width 1
  ?length 1
  )
)
pcell(
Lib.cell.view
(
(Param1 "1234")
(Param2 1234)
)
  Master is lib.vias.layout
  Inst1=Master.place(0:0) with (
  ?width 1
  ?length 1
  )
  Master.place(2:0 1) use Inst1
  ) // parameter reuse
  Master.place(inst.upperRight() 1) use Inst1
  ) // relative placement.
)
Pcell(Lib.vias.view
( (Width 0.5) (Length 0.5) ………
Handle procedure(upperLeft() 0:Length)
)

## Slide 13: New Pcell Structure

## Slide 14: Placement Code
Refer to the right pcell.

## Slide 16: High-Level Code support
Will be linked with synthesis & verification & optimization flow soon.
LAYOUT  High-Level Placement Code is under debugging.

## Slide 17: RFVLSI IDE First Glimps
Support variable scoping checkings.
Support “evaluate-substitution” model checking.
Support syntax highlighting.
Support RFVLSI flow-integrations: (EM, cadence, calibre environment setup, circuit unit test…)
Pcell class function name checks. (parameter checks will be implemented later after flow is ready for better design safty.)