## Slide 1
A Millimeter-Wave RFID Passive Tag IC Using In-Phase Gate-Boosting Rectifier
Speaker：I-No Liao
Advisor：Dr. Yu-Jiu Wang
Research Topic:

## Slide 2: Outline
Introduction
A Millimeter-Wave RFID Tag IC
A Millimeter-Wave In-Phase Gate-Boosting Rectifier
Conclusion and Future Works

## Slide 3
Introduction

## Slide 4: Introduction
RFID system includes
  Tag, reader, and the application system
Application variety is limited mainly by the size of a tag
  This research focuses on designing a small tag
Notes: Introduce RFID system
Application limitation
Operation of the tag (data and energy)

## Slide 5: Introduction
RFID tag size is determined by the antenna
How to reduce the size?
  Use higher operating frequency to shrink the antenna dimensions
  1 mm2 is the target
Why should the size be minimized?
  Increase the variety of RFID applications

## Slide 6: Introduction
Specification of the proposed RFID
  Antenna is shrunk by using 60 GHz downlink and 24 GHz uplink frequencies with one on-chip loop antenna
  1 mm2 tag size is achieved
Item | Specification
Downlink | 60 GHz
Downlink Mode | PWM Modulation
Uplink | 24 GHz
Uplink Mode | FSK Modulation
Data Rate | 200 Mbps
Supply Voltage | 0.6 – 1.2V
Tag Size | 1 mm by 1 mm

## Slide 7
A Millimeter-Wave RFID Tag IC

## Slide 8: A Millimeter-Wave RFID Tag IC
System block diagram
Notes: Introduce all circuit blocks and their functions
Do not emphasize rectifier by now

## Slide 9: A Millimeter-Wave RFID Tag IC
Tag operating flow
  1st working phase: Scavenge energy from surroundings
  2nd working phase: Receive PWM signal – Downlink mode
  3rd working phase: Scavenge energy from surroundings
  4th working Phase: Transmit FSK signal – Uplink mode
The most critical design is the rectifier in this tag
  Increase the tag sensitivity to RF energy in the environment is the design target
Notes: Emphasize the critical block: Rectifier

## Slide 10: A Millimeter-Wave RFID Tag IC
Power Management Unit
  Manage the power supply of other working units by generating Power-On-Reset (POR) signal
PMU works through all four working phases
  PMU must consume little power
  Rectifier must have high RF-to-dc sensitivity
PMU block diagram
Notes: Introduce the operating principle of PMU
Introduce Power-On-Reset (POR) signal
Design concern: Low power consumption and high RF-to-dc sensitivity

## Slide 11: A Millimeter-Wave RFID Tag IC
POR signal simulation
Notes: Explain POR
Voltage sensor monitors VDD by creating Vref and Vcomp

## Slide 12: A Millimeter-Wave RFID Tag IC
60 GHz receiver using PWM demodulator
  Demodulate PWM signal into digital data
  Work in the 2nd working phase – Downlink mode
Receiver block diagram
  Detect 200 MHz envelope of the 60 GHz PWM signal
  Amplified the demodulated signal
  After integration, the digital data are received
Notes: Introduce the operating principle of the receiver

## Slide 13: A Millimeter-Wave RFID Tag IC
PWM demodulator simulation

## Slide 14: A Millimeter-Wave RFID Tag IC
24 GHz FSK transmitter
  Modulate digital data using Frequency Shift Keying
  Work in the 4th working phase – Uplink mode
Transmitter block diagram
  Frequency of VCO is controlled by digital data
  Antenna driver amplifies the signal power
  FSK signal is radiated by the antenna
Notes: Introduce the operating principle of the transmitter

## Slide 15: A Millimeter-Wave RFID Tag IC
How to assure that the power harvested by PMU is enough?
  Total energy stored must be larger than total energy consumed
is the total charge stored at an on-chip capacitor
  and are and in this design
The minimum time required for receiving data
The minimum time required for transmitting data

## Slide 16: A Millimeter-Wave RFID Tag IC
is the battery life for receiver
  is the receiver current consumption in downlink mode
is the battery life for transmitter
  is the transmitter current consumption in uplink mode
For system operation correctness,
This is how data rate, number of bits, and current consumption of receiver and transmitter are determined

## Slide 17: A Millimeter-Wave RFID Tag IC
RFID chip micrograph
  All the pads are for measurement
  In the final tag IC, there will be no pads
  On-chip capacitor
    MoM + MiM capacitors
  The total on-chip capacitance is
  Antenna and on-chip capacitor occupy most of layout area

## Slide 18: A Millimeter-Wave RFID Tag IC
Receiver measurement setup

## Slide 19: A Millimeter-Wave RFID Tag IC
Measured digital data after demodulation
Notes: 180 Mbps is measured

## Slide 20: A Millimeter-Wave RFID Tag IC
Transmitter measurement setup
  Down-conversion is required due to the oscilloscope limit

## Slide 21: A Millimeter-Wave RFID Tag IC
Measured FSK signal
Notes: Explain why the amplitudes are different for different frequency

## Slide 22
A Millimeter-Wave In-Phase
Gate-Boosting Rectifier

## Slide 23: A Millimeter-Wave IGR
The most critical block in RFID tag design: Rectifier
  Rectifier converts RF power into dc supply voltage for the tag
To minimize the tag, 60 GHz is used
  Parasitic capacitance degrades rectifier’s performance
  As the frequency moves higher, parasitic effects impact significantly
Three rectifier design parameters
  Effective threshold voltage
  Forward conducting current
  Reverse leakage current
An In-Phase Gate-Boosting Rectifier (IGR) is proposed to improve RF-to-dc efficiency and sensitivity

## Slide 24: A Millimeter-Wave IGR
Basic Dickson’s rectifier architecture
  Charges are pumped stage by stage

## Slide 25: A Millimeter-Wave IGR
Circuit techniques used in current rectifier designs
  Conventional transistor diode
  Internal Threshold-voltage Cancellation (ITC)
  Active diode
    Forward: Fully turned on
    Reverse: Deeply cut off
  Inductor peaked diode
    and are not in-phase
    is low due to series
    LC-resonant circuit
Notes: Conventional: Vin must be larger than Vth
ITC: Startup problem
Active diode: High speed problem
Inductor peaked: No in-phase is introduced and series LC-resonant

## Slide 26: A Millimeter-Wave IGR
IGR concept
  Amplify swing based on in a passive manner
  Create in-phase condition between and
In multiple-stage IGR
  Use Interleaved ITC (IITC) to reduce threshold voltage
The resulted using IGR
Notes: IGR evolution process
Emphasize that even if there is no ITC, IGR can still reduce Vth to Vth/Av

## Slide 27: A Millimeter-Wave IGR
In-Phase Voltage Multiplier criteria
  It is an impedance conversion network
  The phase of the loaded forward transmission is or
    Note that and are still in-phase
  The last nominal element at the output of the IPVM should be a shunt capacitor
Example
  (a) is the IPVM in differential topology
  (b) is the IPVM in single-ended topology
Notes: Describe the IPVM criteria

## Slide 28: A Millimeter-Wave IGR
Single-transistor IGR
Notes: Explain why Av>1 in (a)(c) and Av<0 in (b)(d)

## Slide 29: A Millimeter-Wave IGR
Single-transistor IGR (Cont.)
  Drain voltage is not always larger than source
  The terminal with a larger swing should be connected to IPVM input
In NMOS case
  When has larger swing then , is preferred
  When has larger swing then , is preferred
In PMOS case
  When has larger swing then , is preferred
  When has larger swing then , is preferred
Notes: Explain why Av>1 in (a)(c) and Av<0 in (b)(d)

## Slide 30: A Millimeter-Wave IGR
Multiple-transistor IGR
  Each single-transistor has its own IPVM: Excessive large area
  The IPVM can be combined to reduce the layout area

## Slide 31: A Millimeter-Wave IGR
ITC topology in the multiple-stage rectifier

## Slide 32: A Millimeter-Wave IGR
Conventional ITC connection

## Slide 33: A Millimeter-Wave IGR
The proposed Interleaved ITC (IITC)

## Slide 34: A Millimeter-Wave IGR
IITC and conventional ITC comparison
Notes: Explain why 3-stage IITC is the best in this design

## Slide 35: A Millimeter-Wave IGR
IGR block diagram and schematic (Schematic is on the next page)
  To ensure a large voltage at the IGR core input terminal, have to be large compared to

## Slide 36: A Millimeter-Wave IGR

## Slide 37: A Millimeter-Wave IGR
Coupling Factor
Effective voltage gain
is contributed by parasitic capacitance from transformer and rectifying transistors
  is the series result of and

## Slide 38: A Millimeter-Wave IGR
AC simulation result of IPVM
Notes: Explain the bandwidth of 52-62 GHz
Describe that ±4 degrees is alright due to a larger voltage gain

## Slide 39: A Millimeter-Wave IGR
IGR transient simulation – In-phase (@ 60 GHz)
Notes: Small reverse current

## Slide 40: A Millimeter-Wave IGR
IGR transient simulation – Out of phase (@ 41 GHz)
Notes: Large leakage current

## Slide 41: A Millimeter-Wave IGR
Potentials of the proposed IGR
Notes: There is still a big margin to improve the proposed IGR by enlarging IGR’s input impedance (Zin1)

## Slide 42: A Millimeter-Wave IGR
Comparisons among several circuit techniques
Notes: Either IITC only or IPVM only overwhelms the conventional rectifier in the same number of stages.
IPVM only performs well in the low input power region. IPVM only is better than IITC+IPVM because IITC has the startup issue.
ITC only performs well in the high input power region.
There is still room to improve if the loss of IPVM can be reduced and Zin1 can be increased.

## Slide 43: A Millimeter-Wave IGR
IGR chip micrograph
  All the pads are for measurement
  IPVM and Input Matching occupy most of layout area
  It will be integrated in RFID tag

## Slide 44: A Millimeter-Wave IGR
S11 measurement
Notes: Explain why the frequency is shifted to 53 GHz
MoM capacitors are not EM simulated (Parasitic itself and wiring parasitic)

## Slide 45: A Millimeter-Wave IGR
Measurement setup #1
  Measure output voltage with various load resistors
  This is the conventional rectifier measurement setup

## Slide 46: A Millimeter-Wave IGR
Broadband measurement with open-loaded IGR
Notes: 46-56 GHz is the 3 dB bandwidth

## Slide 47: A Millimeter-Wave IGR
Measured output voltage with various load resistors
Notes: Explain why the sensitivity drops as the load become smaller

## Slide 48: A Millimeter-Wave IGR
Measured output power and efficiency

## Slide 49: A Millimeter-Wave IGR
Measurement setup #2
  Connect output to a voltage source and measure the output current
  Convenient to find the IGR optimal load resistance

## Slide 50: A Millimeter-Wave IGR
Measured peak output power and efficiency
Notes: Explain that how to calculate the optimal load (Vout/Imeasured). In the design, 10 kOhm is the optimal resistive load.
In practical RFID design, the optimal load is not what we need. We prefer a lower current consumption (larger resistive load).

## Slide 51: A Millimeter-Wave IGR
Measured sensitivity (Target output voltage )
Notes: Connect the result to the RFID tag design

## Slide 52: A Millimeter-Wave IGR
Measured charging curve (Load is )
Notes: Connect the result to the RFID tag design

## Slide 53
Conclusion and Future Works

## Slide 54: Conclusion and Future Works
Performance summary
 | This Work | RFIC 2013 [1] |  |  | JSSC 2010 [2]
Technology | nm | nm |  |  | nm
Die Area | mm2 | mm2 |  |  | mm2
Antenna Type | Loop | Monopole |  |  | N/A
Downlink Frequency | GHz | GHz |  |  | GHz
Downlink Mode | PWM | N/A |  |  | N/A
Uplink Frequency | GHz | GHz |  |  | GHz
Uplink Mode | FSK | OOK |  |  | PWM
Power Scavenging - Rectifier |  |  |  |  | 
Number of stages |  |  |  |  | 
Operating Frequency | GHz |  | GHz | GHz | 
Peak Efficiency | @7 dBm |  | @ dBm | @ dBm | 
Input Sensitivity | dBm @ μA, V |  | dBm @ V | dBm @μA, V | 
 | This Work | RFIC 2013 [1] |  |  | JSSC 2010 [2]
Technology |  |  |  |  | 
Die Area |  |  |  |  | 
Antenna Type | Loop | Monopole |  |  | N/A
Downlink Frequency |  |  |  |  | 
Downlink Mode | PWM | N/A |  |  | N/A
Uplink Frequency |  |  |  |  | 
Uplink Mode | FSK | OOK |  |  | PWM
Power Scavenging - Rectifier |  |  |  |  | 
Number of stages |  |  |  |  | 
Operating Frequency |  |  |  |  | 
Peak Efficiency |  |  |  |  | 
Input Sensitivity |  |  |  |  | 

## Slide 55: Conclusion and Future Works
IGR technique is accept by TMTT 2014
  Title: “A Millimeter-Wave In-Phase Gate-Boosting Rectifier”
Future works
  Antenna design
    On-chip or off-chip?
  Reduce tag power consumption
  Further improve IGR
    Increase number of stages
    Increase input impedance of IPVM
    Reduce ITC power consumption using gate-leakage or sub-threshold methods
Notes: Antenna: On-chip or Off-chip are all possible as long as the size is small enough (Off-chip increases the cost)
Improve IGR: Increase number of stages, Zin of IPVM, and

## Slide 56: Reference
[1] H. Gao, M. Matters-Kammerer, P. Harpe, D. Milosevic, U. Johannsen, A. van Roer-mund, and P. Baltus, "A 71 GHz RF energy harvesting tag with 8% efficiency for wireless temperature sensors in 65nm CMOS," in Proc. IEEE Radio Frequency Integr. Circuits Symp., Jun. 2013, pp. 403-406.
[2] S. Pellerano, J. Alvarado, and Y. Palaskas, "A mm-wave power-harvesting RFID tag in 90 nm CMOS," IEEE J. Solid-State Circuits, vol. 45, no. 8, pp. 1627-1637, Aug. 2010.
Notes: Antenna: On-chip or Off-chip are all possible as long as the size is small enough (Off-chip increases the cost)
Improve IGR: Increase number of stages, Zin of IPVM, and

## Slide 57: Thank you 